## Slide 1: Excel Plots & Trendlines
Week 2 – Day 7

## Slide 2: Line vs. Scatter Plots
Using a “line plot” (as we’ve been doing) implies a known correlation between data points
  REMEMBER, common usage “line graph” means an x-y scatter plot in Excel, with “connect-the-dots” lines
If all we have are data points (no known correlation yet) use a “scatter plot”
  In Excel, this means an x-y scatter plot with no connecting lines
We will determine if there is a correlation by trying to fit a “trend line”

## Slide 3: In-class Exercise #6 Thermocouple Data
Plot the thermocouple data using a “scatter plot”
Predict the temperature reading after 2.75 seconds
  We need to establish a relationship between the thermocouple temperature vs. time.
Time (sec) | Temperature (°C)
1.00 | 65.00
2.30 | 70.00
3.10 | 77.50
4.80 | 117.50
5.60 | 127.50
6.30 | 132.50

## Slide 4: About the data…
The data was taken from J-type thermocouples—Standard grade
Limits of Error in range 0 to 750°C (32 to 1382°F)  2.2°C or 0.75% (whichever is larger)
  Example: At 750°C, error would be ±5.6°C
Thermocouple info:
  http://www.omega.com/techref/thermcolorcodes.html
  http://www.omega.com/thermocouples.html

## Slide 5: Trendline
The line that Excel puts in automatically just “connects the dots” between your data points
How do we get the data trend?
  Use a trendline
  Select data points in graph->right click
  Select Add trendline
  Select type of trendline to add
    Try linear, 2nd order polynomial, exponential

## Slide 6: How do we know if it’s a good fit?
One approach:
  Does curve lie within error bars?
To add error bars:
  Select data points
  Chart ToolsLayoutError Bars icon
  Select height of error bars (2.2%?)

## Slide 7: What else can you do to ensure a good fit?
Look at R2 value
  Select trendline-> right click
  Format trendline-> Display R2 value on chart

## Slide 8: What does R2 value tell us?
R-squared value is the square of the correlation coefficient.
The correlation coefficient, R2, gives a measure of the reliability of the linear relationship between the x and y values.
  R2 = 1 indicates an exact relationship between x and y.
  R2 close to 1 indicate excellent reliability.
  R2 significantly smaller than 1 indicates doubtful usefulness

## Slide 9: Always “sanity check”!
Look at “character” of trendline
  Does it predict negative values…
  Does it predict reversals of slope…
  Does it “roller-coaster”…
  …when the data doesn’t clearly indicate that it should?
Avoiding undesirable features can be more important than achieving a higher R2 value

## Slide 10: Once we have a plot…
If we want to determine the time when a certain temperature is reached…
  Use trend line equation from plot
  Linear interpolation/extrapolation (or FORECAST function in Excel)
  Linear Interpolation:

## Slide 11: Try different curve fits
Second order polynomial
Third order polynomial
Exponential
Most natural phenomena follow linear, exponential, or power-law trends
  Using a higher-order polynomial is frequently a “cop-out” to get a good R2 value without understanding the actual relationship! Use sparingly!

## Slide 12: How do I see the equation for my trendline?
Select trendline
Right click on trendline
Select options tab
  Check display equation on chart box
For exponential, equation takes form of

## Slide 13: In-class Exercise #7
Two pieces of metal are removed from a furnace and placed in a freezer to cool to 0°C. The temperatures of the pieces are measured every 10 seconds following removal from the furnace. The thermocouples used to measure temperature have an uncertainty of 10%. Establish a relationship between the temperature of the part vs. time.
Time (s) | Temp (oC)
0 | 1000
10 | 502
20 | 249
30 | 127
40 | 64
50 | 30
60 | 16
70 | 7
80 | 3
90 | 1